## Slide 1
IN LIECHTENSTEIN

## Slide 2
Programme
        UPS Classification – IEC62040-3
        Power Problems
        Roline UPS Products & Solutions

## Slide 3
IEC 62040-3
A new International UPS Classification by IEC 62040-3
Abstract:
There are three typical UPS circuit arrangements in use, known by their good old names
- On-line UPS or Double Conversion UPS
- Line Interactive UPS
- Off-line UPS or Passive stand-by UPS
but they are not clearly defined.

## Slide 4
Basically, competition is alright – but in case of UPS
designations some competitors are extremely creative!
Terms like “quasi online UPS”, “semi online UPS”, true
online UPS, “online-sharing technology” ...have become
common. The motivation of these UPS providers is to
confuse the user and to make them believe that their products
are true double conversions at a much more affordable price.
In reality, these products are not double conversion, do not
provide the reliability that the user´s expect from double
conversion.
Why a new standard?

## Slide 5
The Problem - Power Line Disturbances
Power Line Disturbance Time scale
1. power output > 10 ms
2. voltage fluctuations < 16 ms
3. voltage transients 4 ... 16 ms
4. under-voltage continuous
5. over-voltage continuous
6. Sporadic lightning effects < 1 ms
7. voltage surges < 4 ms
8. frequency fluctuations sporadic
9. voltage bursts periodic
10. voltage harmonics continuous

## Slide 6
UPS Classification
STEP 1:
UPS output is dependent on the input power grid
STEP 2:
the voltage waveform of the UPS output
STEP 3:
the dynamic tolerance curves of the UPS output

## Slide 7
STEP 1 - Definitions
Step 1: Output Dependency depends on Input supply
Code VFI
Where the UPS ouput is Independent of Input supply Voltage and Frequency variations
VFI Summary - Output voltage is independent of all power line voltage and frequency fluctuations, however remains regulated within the tolerances set forth by IEC 61000-2-4.
This definition is valid for………?

## Slide 8
STEP 1 – Definitions
Step 1: Output Dependency from Input supply
Code VI
Where the UPS output is Dependent on Input Supply Frequency Variations, but supply Voltage variations are conditioned (Independent) ... „
VI Summary - Output voltage is dependent on power line frequency but remains within prescribed limits through active or passive regulating mechanisms.
This definition is valid for………?

## Slide 9
Step 1: by Output Dependency from Input supply
Code VFD
Where the UPS output is Dependent on Input supply Voltage and Frequency variations“
VFD Summary - The UPS output is dependent on changes in power line voltage and frequency when it has no corrective means, such as tapped transformers, EMC filters or variators.
This definition is valid for………?
STEP 1 – Definitions

## Slide 10
STEP 2 - Definitions
Step 2: correlates the output voltage waveform into a simple structure – according to the two operational modes "normal mode " and "standby mode".
Step 2: By generated Output waveform
Code SS: sinusoidal: total harmonics factor D < 0.08 (IEC 61000-2-2) under all linear and under reference non-linear load ..... or
Code XX: Non-sinusoidal: D > 0.08 under reference non-linear load ..... or
Code YY: Non-sinusodial: exeed the limits of IEC 61000-2-2

## Slide 11
STEP 3 - Definition
Business critical applications need a clean sine-wave voltage under all conditions. Step 3 defines the maximum allowable dynamic deviations (from a clean sine-wave). As such, it represents the real "royal challenge" to UPS classification – because this is where the “first class” UPS will be separated from the “rest”.
STEP 3: Three tolerance curves describe the output voltage limits:
Code for Output Tolerance Curves
first character: change of operating mode performance e.g. normal mode–standby mode – bypass mode
second character: step linear load performance in normal / standby mode (worst case)
third character: step non-linear load performance in normal / standby mode (worst case)
1
2
3

## Slide 12
UPS-Topologies
On-Line (Pro Secure)
    perfect regulation
    excellent filter effect
Line-Interactive (Line Secure)
    Line regulation
    good filter effect
Off-Line (Personal Secure)
    works at power failure
    good filter effect
rectifier
inverter
bypass
AVR
Line Filter
Relay-
switch
Battery-
charger
inverter
Line Filter
Relay-
switch
Battery-
charger
inverter

## Slide 13
Roline UPS Products
Classification 3
ROLINE PersonalSecure - VFD
Classification 2
ROLINE LineSecure - VI
Classification 1
ROLINE ProSecure – VFI

## Slide 15
Roline UPSs offer the most reliable and cost-efficient system, to ensure continued protection of connected equipment and supply of electricity by strict quality control.
Our Statement

## Slide 16
Why would I need a UPS?
Roline UPS Products

## Slide 17
Why ROLINE?
Roline UPS Products
1-2-3 concept Easy way for consumers to understand and choose their power protection requirements
Product portfolio Offers a fully reliable product portfolio for all technical products
Software Suite Power Management software with all products
Connection Connectivity options
Solutions not obstacles Not only UPS & Software, but also professional Roline staff and Roline partners

## Slide 18
Grid disturbances and UPS Classes
publicated by ZVEI: UPS Guide

## Slide 19
Product portfolio
Critical, Online
Networking,
Line-interactive
1500*
1000*
800
600
LineSecure
Personal Secure
3000*
2000*
1500
1000*
700
ProSecure
PersonalSecure
SOHO standby
800 500
Roline UPS Products
Class VFD Class VI Class VFI

## Slide 20
Software and Connectivity Products
  To make available a guide for customers with regards to software and connectivity solutions
Software products
  PersonalSecure Includes UPS MON (PC shutdown software)
  LineSecure Includes UPS LAN (Network shutdown software)
  ProSecure Includes UPS LAN (Network shutdown software)
  UPS LAN License for Multi Server Shutdown
Software information (UPS LAN CD)
  Documentation (guides, manuals…)
  Data sheet PDFs (UPS, connectivity..)
  Supported operating charts
Roline UPS Products

## Slide 21
Roline PersonalSecure entry level product for
single PC protection
Product Snapshot
Rating: 500 VA & 800 VA
Voltage: 230 Vac
Frequency: 50 and 60 Hz
Configuration: Tower
Application: Single PC, Workstation
Roline UPS Products
19.40.3505-S PersonalSecure 500VA, 5min, $62,70
19.40.3508-S PersonalSecure 800VA, 3min, $80,81

## Slide 22
Applications: Single PC protection, some special applications where physical size/price matters
Competitors APC ES and CS; Powerware 3110; MGE Pulsar Ellipse, a lot of cheap far-east products
PersonalSecure 500VA, PersonalSecure 800VA
Class VFD, offline technology
PersonalSecure 500 & 800VA bundled with software + signal cable
Approx. 6 min backup time
Key message: *Basic power protection for PC includes shutdown software.
*Ready to use.
Roline UPS Products

## Slide 23
Roline UPS Products
Class VI Line Secure with true Sine-Wave output, Advanced Battery Management and reliable shutdown solution
Product Snapshot
Rating: 600 VA - 1500 VA
Voltage: 220-240 Vac
Frequency: 50 and 60 Hz
Configuration: Tower & 19” Rack
Application: Windows NT/2000 server

## Slide 24
Roline UPS Products
Applications: Office servers, bigger PCs, ATM,s Cold gasoline stations…..
Competitors: APC BackUPS Pro, SmartUPS, Powerware 5115; Pulsar Ellipse Pro, Pulsar Evolution & cheap Far East direct imports
LineSecure 600 VA, 800 VA, 1000 VA* & 1500 VA* * 19” & Standalone Models
Class VI - line-interactive technology
Sine wave output on battery
ABM, Hot swappable batteries, 5 min backup time
External SNMP adapter as option
Key message: *Power protection for office servers that includes reliable shutdown software. *Ready to use.

## Slide 25
Roline Personal Secure vs. Line Secure
When a customer wants to protect a PC, when there is only a need for a reliable Shutdown solution (not necessarily a need for remote monitoring or a multi Server Shutdown), we can offer our
Personal Secure product.
When a customer wants something more and is not willing to pay for a VFI-series (On Line double conversion) our solution is to offer our Line Secure product

## Slide 26
True double-conversion online
protection for any tower application
Product Snapshot
Rating: 700 VA - 3000 VA
Voltage: 208-240 Vac
Frequency: 50 and 60 Hz
Configuration: Tower & 19” Rack
Application: Critical IT application, all industrial applications
Roline UPS Products

## Slide 27
True double conversion online design
  Meets IEC standard 62040-3 regulations for Class 1 double conversion online UPS
  Total independence and complete isolation between input and output for voltage and frequency
Double conversion online is universally
recognized as the most reliable topology
Roline UPS Products

## Slide 28
ProSecure is a VFI-series UPS, LineSecure is a VI-series UPS.
There are more options on ProSecure, ready-made customization is much easier on ProSecure
ProSecure is built to meet industrial applications as well as IT application
      THEREFORE;
When a customer wants to protect anything they consider to be critical, they need to use our product, Roline ProSecure
When the application is Industrial, we can offer Roline ProSecure
Only for bigger projects (when price is an issue), you should offer Roline LineSecure

## Slide 29
Roline UPS Products
RS232 serial communication port
Slot for Connectivity options (work in parallel with either RS232 port)
SNMP/WEB card for option slot
Relay card for option slot
EPO (Emergency Power Off) port (shuts off the outputs)
ProSecure Connectivity

## Slide 30
VALUE UPS Products
Product Snapshot
Rating: 500 VA
Voltage: 230 Vac
Frequency: 50 and 60 Hz
Configuration: Tower
Application: Single PC, workstation
VALUE UPS - entry level product for
single PC protection
Crash Price $39,90
min. Order quantity: 10 pcs. /per Order Available in January 04

## Slide 31
Applications: Single PC protection, some special applications where physical size/price matters
Competitors: Roline LineSecure, APC BackUPS Pro, SmartUPS, Powerware 5115; Pulsar Ellipse Pro, Pulsar Evolution & cheaper
Far-east direct imports
Value UPS 500VA
Class VI, line-interactive technology
Value UPS 500 bundled with software + signal cable
Approx. 6 min backup time
Key message: *Basic power protection for PC which includes shutdown software. Is also ready to use.